## Slide 1: Auto-completion for Writing Network Configurations
Ahsan Mahmood

## Slide 2: Introduction
A network’s backbone is its routing control plane
  Set of rules that dictate how the network should behave
Control plane logic is distributed across the network
Each router has its own configuration file that tells it what to do

## Slide 3: Problem Statement
Network configurations are often very complex
Small mistakes can lead to big problems
Need for tools that can fix broken network configurations or prevent errors

## Slide 4: Possible Solutions
Error-free Internet
Configuration Synthesis
Development Tools
Network Verification
Notes: Present our work in context of the larger goal: a step towards clippy

## Slide 5: Outline
Background
Methodology
Results

## Slide 6
First step

## Slide 7: Autocompletion Engine - Background
Recent research on software systems has shown that codebases tend to contain regularities much like natural languages
  Same combination of words tend to be used more often
Allows us to use Natural Language Processing for code completion
  Neat!
Hypothesis: A similar regularity exists for network configurations
Notes: Researchers have discovered that software systems tend to look like our spoken/written languages in that they contain “regularities” – and by that we mean most of our language uses the same combination of phrases, logic etc.

## Slide 8: What regularity?
Our observations indicate that most of a device’s configuration could be reconstructed from existing configurations
Previous measurement studies have revealed extensive use of templates in network configurations
What do we get?
  NLP on configurations

## Slide 9: Ngram Models
N-grams are simple techniques that allow us to model how likely one token is to follow another one
Using previous tokens, we predict the probability of the next one
We use likelihood estimators to score our N-grams

## Slide 10: Placeholders
We employ a networking- specific optimization predicated by our observation that IP prefixes are often unique to devices
We replace these prefixes and certain other tokens with generic PREFIX tokens

## Slide 11: Testing Methodology
Test on configurations from three large university networks
“Rebuild” the test configurations token-by-token invoking the model at each stage
A prediction is marked as successful when we suggest the correct token within three results
Perform leave-one- out cross validation

## Slide 12: Overall Results
High prediction accuracy (>85%) for the majority of routers.

## Slide 13: Effect of Devices

## Slide 14: Effects of Sample Sizes

## Slide 16: Possible Future Work
Evaluate our model against the current state of the art: tab-completion in CLIs on modern routers
Using larger n-grams to suggest complete statements
Completing entire lines or even stanzas
Not just based on syntax but also desired goals using input from operators

## Slide 17: Thank you?

## Slide 18: Possible Solutions
Error-free Internet
Configuration Synthesis
Development Tools
Network Verification
Templates
Writing Assistant