## Slide 1: Auto-completion for Writing Network Configurations
Ahsan Mahmood, Aaron Gember-Jacobson

## Slide 2: Introduction
A network’s backbone is its routing control plane
  Set of rules that dictate how the network should behave
Control plane logic is distributed across the network
Each router has its own configuration file that tells it what to do

## Slide 3: Problem Statement
Network configurations are often very complex
Small mistakes can lead to big problems
Need for tools that can fix broken network configurations or prevent errors

## Slide 4: Possible Solutions
Error-free Internet
Configuration Synthesis
Development Tools
Network Verification
Command Line Interfaces
Templates
Notes: Present our work in context of the larger goal: a step towards clippy

## Slide 5: Outline
Background
Methodology
Results

## Slide 6: Network Configurations - Background
Example Cisco Configuration
What can we infer?
  Device name is B
  Access control list will deny any IP address starting with 12
  Connected to two other routers
!
version 12.4
!
hostname B
!
access-list 1 deny 12.0.0.0 0.255.255.255
access-list 1 permit any
!
interface GigabitEthernet0/1
description INFRA:C:Gi0/1
ip address 1.0.1.1 255.255.0.0
ip ospf cost 1
ip access-group 1 in
!
router ospf 1
redistribute connected
network 3.0.0.0 0.0.255.255 area 0
network 1.0.0.0 0.0.255.255 area 0
!
end
Stanza
Token
IP Address
Notes: What are the rules?

## Slide 7: Our Vision
Writing assistant for building network configurations
  Think Clippy for networks! (But not as terrible)
Ambitious goals
  Suggests complete stanzas
  Automatically fills in parameters
  Suggests improved syntax
This thesis works towards a concrete first step
  Suggesting tokens!
Notes: Improved/concise
We want all of this, so where do we start? Tokens!

## Slide 8: Challenges
Routers have different roles
Configurations often have many parameters which add variance
We may need long histories of snapshots
Some networks may not have any existing configurations to help build a model
Notes: Roles: core (w/in Colgate) vs edge (for internet)
Parameters: such as device name – go back to explain

## Slide 9: Autocompletion Engine - Background
Recent research on software systems has shown that codebases tend to contain regularities much like natural languages
  Same combination of words tend to be used more often
Allows us to use Natural Language Processing for code completion
  Neat!
Hypothesis: A similar regularity exists for network configurations
Notes: Researchers have discovered that software systems tend to look like our spoken/written languages in that they contain “regularities” – and by that we mean most of our language uses the same combination of phrases, logic etc.

## Slide 10: What regularity?
Most of a device’s configuration can be reconstructed from existing configurations
Previous measurement studies have revealed extensive use of templates in network configurations
What do we get?
  NLP on configurations
Notes: Our observations indicate that most of a device’s configuration could be reconstructed from existing configurations

## Slide 11: N-gram Models
N-grams are simple techniques that allow us to model how likely one token is to follow another one
Using previous tokens, we predict the probability of the next one
We use likelihood estimators to score our N-grams

## Slide 12: Placeholders
We employ a networking- specific optimization predicated by our observation that IP prefixes are often unique to devices
We replace these prefixes and certain other tokens with generic prefix tokens
!
version 12.4
!
hostname B
!
access-list 1 deny IPADDRESS SUBNET
access-list 1 permit any
!
interface GigabitEthernet#ID
description DESCRIPTION
ip address IPADDRESS SUBNET
ip ospf cost 1
ip access-group 1 in
!
router ospf 1
redistribute connected
network IPADDRESS SUBNET area 0
network IPADDRESS SUBNET area 0
!
end
Notes: Engine can help you figure out whether you need ipadress here or not

## Slide 13: What about our data?
“It’s not my fault. Our data sucks!”
- Me from the past
“We don’t have better algorithms. We just have more data.”
- Peter Norvig

## Slide 14: Our cute little dataset
Figure 1: Our data contains a myriad of configuration sizes

## Slide 15: Our cute little dataset
Table 1: Acquired configurations from three large university networks
University | Number of Configurations | Total Lines | Average Lines
A | 35 | 73K | 2.1K
B | 26 | 61K | 2.3K
C | 24 | 67K | 2.8K

## Slide 16: Testing Methodology
“Rebuild” the test configurations token-by-token
A prediction is marked as successful when we suggest the correct token within three results

## Slide 17: Testing Methodology
. . .
!
access-list 1 deny IPADDRESS SUBNET
access-list 1 permit any
!
interface GigabitEthernet#ID
description DESCRIPTION
ip address IPADDRESS SUBNET
ip ospf cost 1
ip access-group 1 in
!
router ospf 1
redistribute connected
network IPADDRESS SUBNET area 0
network IPADDRESS SUBNET area 0
!
end
. . .
!
access-list 1 deny IPADDRESS SUBNET
access-list 1 permit any
!
interface GigabitEthernet#ID
description DESCRIPTION
ip
ospf
address
ssh
address

## Slide 18: Testing Methodology
“Rebuild” the test configurations token-by-token
A prediction is marked as successful when we suggest the correct token within three results
Perform leave-one-out cross validation

## Slide 19: Overall Performance
Figure 1: High prediction accuracy (>85%) for the majority of routers.

## Slide 20: Challenges
Routers have different roles
Configurations often have many parameters which add variance
We may need long histories of snapshots
Some networks may not have any existing configurations to help build a model
Notes: Roles: core (w/in Colgate) vs edge (for internet)
Parameters: such as device name – go back to explain

## Slide 21: How well did our placeholders perform?
Figure 2: Placeholders improve accuracy by 5% higher.
Notes: Diminishing returns

## Slide 22: How does the model perform for small datasets?
Figure 3: Smaller sample sizes give surprisingly high accuracies

## Slide 23: What about different router roles?
Figure 4: Models trained on different roles don’t seem to fare much better than our overall average

## Slide 24: Possible Future Work
Evaluate our model against the current state of the art: tab-completion in CLIs on modern routers
Using larger n-grams to suggest complete statements
Completing entire lines or even stanzas
Not just based on syntax but also desired goals using input from operators

## Slide 25: Thank you!

## Slide 26: How does the model perform for small datasets?
Figure: Smaller sample sizes give surprisingly high accuracies